IMPLEMENTATION

Configuration for hardware and software

        It doesn't need any additional hardware or software to operate the program,but the following requirements should be strongly maintained:

   Requirements for hardware:

1. Pentium II or higher.
2. 512MB of RAM or higher.
3. 800MHz processor or above.
4. 20 MB of hard disk space.

  Requirements for software:

1. Operating System LINUX or WINDOWS.
2. Python 2.* or higher with pygtk.

About Program Logic:
Although adders can be constructed for many numerical representations, such as binary-coded decimal or excess-3, the most common adders operate on binary numbers.
But the adder we are implementing is for the decimal numbers. We have implemented it using two models.
1. The Ripple Carry Adder (using circular linked list)
2. The Carry Look Ahead Adder (using arrays)

1.Ripple Carry Adder

The two input numbers are stored in a circular linked list. The number is traversed from right to left adding them bit by bit. A variable carry is set if the sum ((sum)A = A + B + Carry) is greater than 10 or else it is 0. Sum modulo 10 is taken to get the sum bit . In this way, the whole list is traversed with carry rippling to the next bit. The final answer ie the sum is stored in one of the input list.

2. Carry Look Ahead Adder

To reduce the computation time, engineers devised faster ways to add two binary numbers by using carry-look ahead adders. They work by creating two signals (P and G) for each bit position, based on whether a carry is propagated through from a less significant bit position (at least one input is a '1'), generated in that bit position (both inputs are '1'), or killed in that bit position (both inputs are '0'). In most cases, P is simply the sum output of a half-adder and G is the carry output of the same adder. After P and G are generated the carries for every bit position are created.
A carry-lookahead adder improves speed by reducing the amount of time required to determine carry bits.
The same logic has been implemented using C on decimal numbers.
Here, G = (A + B)/10 and P = (A+B)%10..
Carry is generated simultaneously using the recurrence relation
 C[i] = G[i] | ((P[i] == 9) ? C[i-1] : 0 where, i>=1.